## Slide 1
PERSONAL PHONE VIDEO → HAND MOTION → PANDA MANIPULATION
Phone-to-Panda
Data-Efficient Human-to-Robot Retargeting from Self-Collected Hand Motion
Google Colab • Python • MediaPipe • MuJoCo 3.15.0 • Franka Panda

## Slide 2
The challenge and the design choice
Translating personally collected human demonstrations to robotic execution.
PERSONAL DATA
12 videos
Recorded using a phone camera showing side-profile manipulation of an orange cube and wooden box.
ROBOTIC TASK
Pick → carry → release
Executing a structured pick-and-place sequence in MuJoCo simulation with the Franka Panda arm.
CORE IDEA
Retarget human motion
Directly mapping wrist position and pinch distance to Cartesian targets without large learned policy models.
Design Rationale & Simplicity
The five-finger human hand is intentionally reduced to wrist position plus a pinch/open signal. This avoids complex multi-joint direct kinematic mapping and enables robust transfer to a different robotic embodiment without requiring large learned policy models or black-box neural networks.

## Slide 3
Personal dataset
The final demonstration uses one of 12 self-recorded phone videos.
12
Videos Collected
Self-recorded side-profile phone videos
267
Source Frames
Total frames in demonstration video IMG_2343.MOV
30 FPS
Frame Rate
Standard high-definition capture frequency
8.9 s
Duration
Complete demonstration time span
155
Detected Frames
Frames with successful MediaPipe hand tracking
58.05%
Detection Rate
Robust tracking efficiency across source video
Data Management Note: Original personal videos remain private. The public project repository uses derived landmark/trajectory CSVs and final simulation outputs rather than raw video assets.

## Slide 4
From phone video to robot trajectory
A robust four-stage transformation pipeline.
01
MediaPipe
Extracts up to 21 hand landmarks per detected frame from video.
02
Features
Reduces high-dim hand representation to wrist X/Y + pinch distance.
03
Events
Analyzes adaptive pinch threshold to detect grasp (~4.47s) and release (~6.47s).
04
Retargeting
Maps human progress between start/end Cartesian positions into 25 samples.
Key Architectural Decision
The human signal controls motion progress, not raw robot joint angles. This decoupled approach ensures absolute stability and prevents dangerous kinematic singularities during execution.

## Slide 5
MuJoCo Panda manipulation
Executing the pick-and-place task in MuJoCo 3.15.0 simulation.
1. GRASP
Move Panda hand to mapped grasp point [0.4354, 0.0, 0.4050] m.
2. CARRY
Follow the 25 retargeted trajectory points smoothly.
3. RELEASE
Move above target box and open gripper.
4. PLACE
Perform controlled cube descent into green target box.
SIMULATION ENVIRONMENT
Franka Emika Panda & MuJoCo 3.15.0
• Robot starts from joint config [0, -0.5, 0, -2, 0, 1.5, 0.7] • Uses damped Jacobian inverse kinematics (sub-millimetre IK error: 0.198 mm) • Simplified deterministic grasp model: Cube follows hand while grasped to isolate retargeting from contact physics instability.

## Slide 6
Results
The final complete run successfully completed the pick-and-place task.
25
Retargeted Samples
Extracted trajectory points
145
Simulation States
Total states in final video
0.198 mm
Grasp-Target Error
High precision target reaching
0.000 mm
Horizontal Error
Final X-Y placement accuracy
0.000 mm
Vertical Error
Final Z placement accuracy
TRUE
Task Success
Cube successfully placed in box
Final Cube Position: [0.55, 0.10, 0.355] m | Box Centre: [0.55, 0.10, 0.36] m — Cube confirmed inside target box.

## Slide 7
What worked — and what did not
Honest engineering assessment of system capabilities and limitations.
WHAT WORKED
• Personal phone data directly dictates robot trajectory.
• MediaPipe provides an inexpensive, robust hand motion extractor.
• Pinch distance gives a clean, interpretable grasp/release signal.
• Damped Jacobian IK reaches target with sub-millimetre error.
• Lightweight implementation runs seamlessly in Google Colab.
LIMITATIONS & TRADEOFFS
• Hand detection rate of 58.05% due to occasional occlusion.
• Simplified grasp mechanism rather than contact-rich physics.
• No large VLA model, reinforcement learning, or world model.
• Embodiment abstracted to wrist trajectory + gripper state.
• Simulation demonstrates retargeting rather than physics grasping.

## Slide 8
CONCLUSION
A small personal dataset can drive a meaningful robotics signal.
Phone video → Hand landmarks → Grasp signal → Retargeted Panda motion → Successful placement
The contribution is not model size. It is a simple, reproducible way to make personally collected human data drive a different robotic embodiment.
Repository: phone-to-panda | README + notebook + source + derived data + results